## Slide 1
Testing, utvikling og bruk av oljevernutstyr i kaldt klima
Av Per-Arne Sundsbø
Professor – Teknologi i kaldt klima
UiT – campus Narvik
FoU innen marine operasjoner i kaldt klima ved UiT-Narvik:
Utvikling av analyseverktøy, tekniske løsninger og prosedyrer
Testing & verifisering ift kravspesifikasjon (metocean)

## Slide 2
FoU-prosjekter UiT- Narvik
Offshore & onshore vinterisering
Melkøya: Snødrift, vindavkjøling, ising på kai ++
Goliat-livbåt: Testing sjøsprøytising ++
Castberg field : Testing snø og is på gratings
Shtokman: Design av vent panel mht snøinndrev/is og diverse vinterisering
Shakalin II: Design for ising, snødrift ++
Barentshavet (BASOP): Sjøsprøytising på oljeverns-utstyr for Goliat, Johan Castberg and Wisting

## Slide 3
Utfordringer oljevernutstyr i kalde farvann
Kulde endrer materialegenskapene
Ising/sjøsprøytising reduserer eller ødelegger funksjon på utstyr
Utendørs arbeidsmiljø/menneskelige faktor sterkt påvirket av kombinerte effekter fra kulde, vind, nedbør, is, mørke, remoteness m.m.

## Slide 4
Eksempel på utfordringer i kalde farvann
Testing av ubemannet overflatefartøy (USV)
System | Function /requirements | Accept criteria | Comment
Ice build-up on topside/structure | Positive stability | Max X mm of ice | 
Hatches | Possible to open the hatch | Possible to open | Often a challenge caused by frozen condensed water or sea spray ice
Sensors, radar and antennas for communication | Measure, transmit & receive | Being operative. | The effect of icing should be investigated
Marker/navigation lights | Must be visible for other ships Luminous intensity of min. x.x candela. Flash rate of x – x per minute | Must not be covered by ice. | 
Air inlet for engine (or any vent system) | Provide sufficient airflow | Necessary volume of air possible to get thru the inlet. | Engine might stop?
Fuel tank ventilation | Provide sufficient ventilation for fuel tank | Complete free of ice. Open for ventilation. | 
Bailing/bilge pump outlet (if on vessel) | Must be possible to pump out water | Opening complete free of ice. | 
Towing/painter hook | Must be possible to connect to | Free of ice | Critical for retrieving of vessel at sea
Towing line/painter system (if on vessel) | Possible to release rope. | Hatch/system not blocked by ice | Towing line could be frozen caused condensed water
++++ |  |  | 

## Slide 5
Ising på fartøy og marine strukturer
Marin ising når sjø eller dråper treffer en kald overflate og fryser.
To hovedtyper – Sjøsprøyt og atmosfærisk ising
Sjøsprøytising er mest opptredende og viktigst
Ising kan også oppstå fra sjø som strømmer inn over dekk
Vindgenerert sjøsprøyt
Sjøsprøyt generert av skip-bølge-vind effekter

## Slide 6
Ising på fartøy og marine strukturer
Komplisert prosesser (vind-bølge-skip interaksjoner)
Ising på skip øker generelt med økende vind, kulde og sjøsprøyt
Tilstrekkelig mengder sjøsprøyt & overskylling vil igjen motvirke ising
Generelt mindre data ift ising på oljevernutstyr i sjøen

## Slide 7
Metoder for testing & verifisering
Fullskala – gir de mest realistiske resultater (omfattende dyrt, værbegrensninger)
Kaldt klima lab – god kontroll og fleksibilitet med test-parametre
Modelleringsverktøy – som numeriske simuleringer benyttes sammen med forsøk
  Pga begrensninger og fordeler med individuelle metoder, er det oftest mest hensiktsmessig å kombinere alle.
Video 1: LenseWave.avi
Numerical simulation of NO-1200-S in waves

## Slide 8
Sjøsprøytising på antenne AIS bøye
AIS-bøye sjøsettes i oljeutslipp for å overvåke utslippet bevegelser.
Testing utført mht eventuell tap i signalstyrke pga ising på antenne:
Påføring av sjøsprøyt/is under kontrollerte forhold i lab (2, 3.5 og 7 mm is).
Utendørs testing av signalstyrke utført av Nasjonal kommunikasjonsmyndighet (Nkom) og synlighet på MarineTraffic .
Resultat: Testede istykkelser reduserte ikke signalstyrken. Mulig årsak er at antenna ikke er tilpasset aktuelle bølgelengder (Nkom).

## Slide 9
Oljevernutstyr i kaldt klima
Ising på utstyr i sjøen
Bevegelser i sjø og utstyr/duk, og bølgevasking reduserer ising.
Større risiko der utstyret blir liggende i ro inne i fjorder, ved lavere temperaturer og mindre saltinnhold i sjøen.
Oljevernutstyr på dekk
Dekk og rigg kan være mye utsatt for ising og kulde, men effektive beskyttelsestiltak eksisterer.

## Slide 10
Oljevernutstyr i kaldt klima
Oljevernberedskapen i kalde farvann er mer avhengig vår total evne til å utføre operasjoner under tøffe værforhold.
«Vinterisering» av fartøy og dekksutstyr som kraner o.l..
Utendørs arbeidsoperasjoner bør identifiseres og reduseres til et minimum.

## Slide 11
Bruk av sjøvann for avising/hindre ising
Eksisterende metoder på fartøy:
Provoserende skipsmanøvrer (øke frekvens sjøsprøyt, ramming av større bølger)
Spyling/overstrømming av havvann på dekk
Ny forskning viser at bruk av havvann for avising kan ha et stort potensial (ref. Ane Sæterdal, Skarheim etc )

## Slide 12
Avising med sjøvann via sprinkelanlegg
Testing whether the top mounted fire sprinkler system on the FF1200 Goliat lifeboat is may be used for deicing and the potential effectiveness.
Acceptance criteria:
Removal of ice from canopy.
Sprinkler system drains after test / Sprinkler nozzles not frozen.
Airtemp= -8.7 °C
Sea temp= 3.5 °C
Salinity= 31.1 ‰
From the full-scale measurement campaign in Ofotfjorden on a FF1200 lifeboat, 2017-2018.

## Slide 13
Avising med sjøvann via sprinkelanlegg
Sea spray icing on sprinkler nozzles and canopy surface at the FF1200 during the full-scale measurement campaign in Ofotfjorden.
Due to plus degree sea water temp and driving sprinkling water pressure, the frozen nozzles did melt and reopen during the sprinkler-test the following day.
Sea spray icing on sprinkler nozzles and canopy surface at the FF1200 (Photo: Jan-Arne Pettersen, UiT)
Sundsbø, P.A., Jacobsen, T. and Safer, R., 2018, FF1200 Test report Sea Spray Icing on Goliat Lifeboat, Palfinger Marine Safety AS, Palfinger report 5583.

## Slide 14
Sæterdal, A., Visich, A., Deshpande, S. & Sundsbø, P.A., 2023, Experimental investigation of deicing with seawater, Submitted to ISOPE
Avising med sjøvann via sprinkelanlegg
Before & after deicing of Viking Norsafe Miriam 8.5 lifeboat using sprinkling seawater.

## Slide 15
Utvikling av bedre modelleringsverktøy
Numeriske modellering av sjøsprøyt gjennom wind-wave-ship interaction
- Nyttig verktøy for utvikling av nye design og løsninger
Video 2: Seaspray.avi
Video 3: Seaspray.avi

## Slide 16
Utvikling av bedre modelleringsverktøy
Numeriske modellering av ising på overflaten ved hjelp av Kunstig Intelligens (KI) metode
Den svært kompliserte isingsprosessen erstattes KI-metode og data fra lab som input
Kan være en «game changer» innen modellering av sjøsprøytising o.l.
Sea spray icing modelling concept based on CFD and Machine learning or classic approach.

## Slide 17
Sea spray experimental data for ML-model
Sea spray experiments in UiT-cold climate lab provides data to the ML-model for evaluation of icing at probe locations on ship surface.
Basic idea is that the icing in lab represents the icing on vessel.
(Deshpande, Sæterdal & Sundsbø, 2023)

## Slide 18
Utvikling av framtidas oljevernberedskap
FoU-prosjekt - Sikre heli-landinger på havis
Under planlegging i samarbeid med Cold Regions Research and Engineering Laboratory (CRREL)
Helikopter fra m/v Ortelius på Antarktis (Oceanwide Expeditions News 23.01.2013)
Video 4: SARQueen.mp4

## Slide 19
Avsluttende bemerkninger
Utvikling av lenser, trål o.l. for større vannhastighet kan redusere faren for ising.
Mer nøyaktige og mer omfattende vær/isingsvarsler
Teknologisk utvikling med stadig bedre vinteriserte skip og løsninger (gode fiskepriser?).
Nye verifiserte simuleringsverktøy for sjøsprøytising vil ikke erstatte forsøk og fysisk testing, men gir et større potensiale for utvikling.
Økende samarbeid mellom de største aktørene (utvikling & info).
Mer privatisering av offentlige aktører som Kystverket, kan pulverisere ansvar.
Menneskelige faktor, med generell erfaring fra drift & øvelser vil fremdeles være den viktigste faktor (som forsker kan jeg ikke få nok fullskaladata )

## Slide 20
Acknowledgements
The author(s) would like to thank Palfinger Marine Safety for providing the FF1200 lifeboat equipped and prepared for the Goliat field in the Barents Sea. We would also like to give special thanks to Eni with Rheda Safer and Leif Brede Sømme for steering, financing and being involved in the planning of the full-scale measurement campaign.
The authors also wants to thank PHD Researcher Shayan Dadman at the UiT for providing valuable support related to the machine learning modelling.

## Slide 21
Bibliography/references
Andreas, E.L., 1998, A New Sea Spray Generation Function for Wind Speeds up to 32 m s21, J O U R N A L O F P H Y S I C A L O C E A N O G R A P H Y VOLUME 28.
Deshpande S., Sæterdal ., Sundsbø P.A., 2023, Experiments with Sea Spray Icing: Investigation of Icing Rates, Journal of offshore Mechanics and Arctic Engineering, February 2024, 146(1) / 011601, Paper number OMAE-22-1165. Published online: May 11, 2023. https://doi.org/10.1115/1.4062255Fenton, J.D., 1985, A Fifth-Order Stokes Theory for Steady Waves, Journal of Waterway, Port, Coastal and Ocean Engineering, Vol. 111, No. 2.
Fenton, J.D., 1999, Numerical Methods for Nonlinear Waves, Advances in Coastal and Ocean Engineering, Vol. 5, ed. P.L.-F. Liu, pp. 241-324, World Scientific: Singapore.
FLOW-3D®, 2024, Flow-3D Version 12.0.3 [Computer software], Santa Fe, NM: Flow Science, Inc., https://www.flow3d.com.
Hirt, C.W. & Sicilian, J.M., 1985, A porosity technique for the definition of obstacles in rectangular cell meshes, Proceedings of the fourth International Conference on Ship Hydrodynamics, Washington, D.C.
Hirt, C.W. & Nichols, B.D., 1981, Volume of fluid (VOF) method for dynamics of free boundaries, Journal of Computational Physics, 39, 201–225.
Hirt, C.W., 1993, Volume-fraction techniques: Powerful tools for wind engineering. J. Wind Eng. Indust. Aero., 46–47, 327–338.
Kudryavtsev, V. N. and Makin, V. K., 2009, Model of the spume sea spray generation Geophysical Research Letters, VOL. 36, L06801, doi:10.1029/2008GL036871.
Kulyakhtin, A., 2014, “Numerical Modelling and Experiments on Sea Spray Icing,” Doctoral thesis, Department of Civil and Transport Engineering, Norwegian University of Science and Technology (NTNU), Norway.
Samuelsen, E. S., Edvardsen, K. and Graversen, R.G., 2017, Modelled and observed sea-spray icing in Arctic-Norwegian waters, Cold Regions Science and Technology 134 (2017) 54–81.
Sundsbø, P.A. and Deshpande, S. , 2024, Investigation into using CFD for estimation of ship specific parameters for the SPICE model for prediction of sea spray icing. Part 2: Verification of SPICE2 with full scale test (to be submitted).
Sundsbø, P.A., Jacobsen, T. and Safer, R., 2018, FF1200 Test report Sea Spray Icing on Goliat Lifeboat, Palfinger Marine Safety AS, Palfinger report 5583.
USACE, 2008, “Coastal Engineering Manual Part II, 1.” EM 1110-2-1100. U.S. Army Corp of Engineers.
Wei, G., 2005, A fixed-mesh method for General Moving Objects in Fluid Flow, Modern Physics Letters B, Volume 19, Issue 28-29, pp. 1719-1722.
Yakhot, V.; Orszag, S.A.; Thangam, S.; Gatski, T.B.; Speziale, C.G., 1992, Development of turbulence models for shear flows by a double expansion technique, Phys. Fluids A, 4, 1510–1520.